09.10.2008

Scanning time of B6 control board

At the B6, the general scanning time of the control board is 10ms.

Only I1 can be adjusted to a scan time between 2ms and 10ms. To do so, the parameter di.23 (fast digital noise filter) in the application mode can be adjusted accordingly.

-1 = OFF	( no noise filter, resulting in a scan time of approx. 10ms

0 ms		( noise filter of 0ms, resulting in a scan time of approx. 2ms

The B6 Config-ID is 5136.